# Moxa UC-771x for dummies
## What is linux?
Linux is an operating system. It consists of a "kernel" and various "userland" applications. A Linux system can be easily stripped down or extended. This makes it suitable for desktop, server and embedded applications. All Linux systems are based on the Linux kernel. The Linux kernel is the base of the operating system and contains memory management, drivers and other basic functionality. The Linux kernel can be extended by loading modules. This way drivers or NAT functionality can be added to the kernel.
## How to connect
There are two ways to connect to the Moxa:
Serial:
Shows boot messages
- Relatively slow
- Direct cable connection
Telnet
- Easy to connect
- Able to use in a remote access session
- Fast
Not suitable to solve network/firewall issues

The best program to connect to the moxa is putty (www.putty.nl).
Putty can be installed and used "portable".
### Serial
1. Open putty
2. Select on the right side of the radio box "serial"
3. Enter the correct serial port and speed (19200)
4. Click "Open"

### Netwerk
1. Open putty
2. Select the radio box "telnet"
3. Fill in "Host Name" (the IP address of the moxa)
4. Click "Open"

## The commandline
After the making of a connection a so-called “login prompt” is displayed.
Default login credentials:
login: root
Password: root

Basic commands for navigation and simple file operations are:
ls	List a file or the content of a directory
chmod	Change flags and permissions
cp	Copy files or directories
mv	Move (or rename) files or directories
rm	Remove files or directories
cat	Concatenate files and print their contents
head/tail	output the first/last part of files
cut	remove sections from each line of files
grep	print lines matching a pattern
ps	report a snapshot of the current processes.
kill	terminate a process
vi	Text editor
ifconfig	configure a network interface
iptables	administration tool for IPv4 packet filtering and NAT

### General usage tips
#### Use the TAB-key:
By pressing <TAB> the shell completes your words/commands/file names.
Pressing <TAB> twice show all possible completion options.
Example:
#ipt<TAB>
#iptables
#iptables<TAB><TAB>
iptables iptables-restore iptables-save
#iptables
Example:
#cd /e<TAB>
#cd /etc/<TAB><TAB>
/etc/cron.d/	/etc/dhcpc/
#cd /etc/d<TAB>
#cd /etc/dhcpc/
Tab-completion “understands” that the command “cd” requires a file/directory name as argument and uses them for completion.
When completing commands, pressing the <TAB> key only shows executable files. (Programs or files with the executable flag set).
#### Wildcards:
Use the “*” chracter to indicate multiple files with similar names:
# ls net/ipv4/netfilter/ip_*.ko
net/ipv4/netfilter/ip_tables.ko
net/ipv4/netfilter/ip_nat_tftp.ko
net/ipv4/netfilter/ip_nat_snmp_basic.ko
net/ipv4/netfilter/ip_nat_irc.ko
net/ipv4/netfilter/ip_nat_ftp.ko
net/ipv4/netfilter/ip_nat_amanda.ko
net/ipv4/netfilter/ip_nat.ko
#

#### Options:
Commands usually have different options. Options are preceded with a “-” character:
# ls /
ramdisk proc usr tmp lib dev
sbin home var mnt etc bin
# ls -l /
lrwxrwxrwx 1 root root 12 Feb 1 2008 ramdisk -> /mnt/ramdisk
lrwxrwxrwx 1 root root 4 Feb 1 2008 sbin -> /bin
dr-xr-xr-x 32 root root 0 Jan 1 1970 proc
drwxr-xr-x 3 root root 0 Feb 1 2008 home
drwxr-xr-x 3 root root 0 Feb 1 2008 usr
drwxr-xr-x 8 root root 1024 Jan 1 1970 var
lrwxrwxrwx 1 root root 8 Feb 1 2008 tmp -> /var/tmp
drwxr-xr-x 4 root root 0 Feb 1 2008 mnt
drwxr-xr-x 3 root root 0 Feb 1 2008 lib
drwxr-xr-x 4 root root 0 Jun 12 14:00 etc
drwxr-xr-x 3 root root 0 Feb 1 2008 dev
drwxr-xr-x 2 root root 0 Feb 1 2008 bin
#### HELP!:
The option “--help” usually shows a short description of the different options and usage of a command.
#### Pipe:
The “|” character (shift+\) pipes the output of one command to another command. This can be used to filter the output of a command:
# ps |grep ps
  203 root RW ps
  204 root RW grep ps
# ps |grep ps|cut -d” “ -f 3,4
  203 root
  204 root
#### Redirect output:
It is possible to redirect output of a command to a file. This is done using the “>” character. A single “>” overwrites any existing file whereas a double “>>” appends to it.
# ifconfig > ip-configuratie.txt
# cat ip-configuratie.txt
eth0 Link encap:Ethernet HWaddr 00:90:E8:15:8A:9E
        inet addr:172.16.1.101 Bcast:172.16.255.255 Mask:255.255.0.0
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        RX packets:486 errors:0 dropped:0 overruns:0 frame:0
        TX packets:1477 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000
# echo test > ip-configuratie.txt
# cat ip-configuratie.txt
test
# ifconfig >> ip-configuratie.txt
# cat ip-configuratie.txt
test
eth0 Link encap:Ethernet HWaddr 00:90:E8:15:8A:9E
        inet addr:172.16.1.101 Bcast:172.16.255.255 Mask:255.255.0.0
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        RX packets:486 errors:0 dropped:0 overruns:0 frame:0
        TX packets:1477 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000

### Permissions
Long listings show a range of letters at the beginning of each line:
drwxr-xr-x 3 root root 0 Feb 1 2008 dev
The first letter indicates whether it concerns a file (-) or directory (d). The following 9 letters indicate the file/directory's permissions. These 9 letters are divided into three groups: User, Group and Others. The letters within these groups represent permission flags and can be either on of off. The order of these letter is always the same.
rwx: Read, Write, eXecute
Since these permission letters can be either on or off, they can be seen as a binary code. Every group of three letters can be translated to one number between 0 and 7. This is done by adding the bit-value of every permission that is set:

r	w	x
4	2	1

The numeric representations of the three permission groups can then be concatenated into a three digit numerical representation. For example:
Letters	Numerical
rwxr-xr-x	755
rwxr-x---	750
rw-r--r--	644

### Uitleg commandos
### ls
ls [-1AacCdeFilnpsTtuwxk] [FILE]...
List directory contents
Options:
        -1 List in a single column
        -A Don't list . and ..
        -a Don't hide entries starting with .
        -C List by columns
        -c With -l: sort by ctime
        -d List directory entries instead of contents
        -e List full date and time
        -F Append indicator (one of */=@|) to entries
        -i List inode numbers
        -l Long listing format
        -n List numeric UIDs and GIDs instead of names
        -p Append indicator (one of /=@|) to entries
        -s List the size of each file, in blocks
        -T NUM Assume tabstop every NUM columns
        -t With -l: sort by modification time
        -u With -l: sort by access time
        -w NUM Assume the terminal is NUM columns wide
        -x List by lines

chmod
chmod [-Rcvf] MODE[,MODE]... FILE...
Each MODE is one or more of the letters ugoa, one of the symbols +-= and one or more of the letters rwxst
Options:
        -R Recurse

cp
cp [OPTIONS] SOURCE DEST
Copy SOURCE to DEST, or multiple SOURCE(s) to DIRECTORY
Options:
        -a Same as -dpR
        -d,-P Preserve links
        -H,-L Dereference all symlinks (default)
        -p Preserve file attributes if possible
        -f Force overwrite
        -i Prompt before overwrite
        -R,-r Recurse
        -l,-s Create (sym)links
mv
mv [OPTIONS] SOURCE DEST or: mv [OPTIONS] SOURCE... DIRECTORY
Rename SOURCE to DEST, or move SOURCE(s) to DIRECTORY
Options:
        -f Don't prompt before overwriting
        -i Interactive, prompt before overwrite
rm
rm [OPTIONS] FILE...
Remove (unlink) the FILE(s). Use '--' to indicate that all following arguments are non-options.
Options:
        -i Always prompt before removing
        -f Never prompt
        -r,-R Remove directories recursively

cat
cat [-u] [FILE]...
Concatenate FILE(s) and print them to stdout
Options:
        -u Use unbuffered i/o (ignored)
tail
tail [OPTIONS] [FILE]...
Print last 10 lines of each FILE to standard output. With more than one FILE, precede each with a header giving the file name. With no FILE, or when FILE is -, read standard input.
Options:
        -c N[kbm] Output the last N bytes
        -n N[kbm] Print last N lines instead of last 10
        -f Output data as the file grows
        -q Never output headers giving file names
        -s SEC Wait SEC seconds between reads with -f
        -v Always output headers giving file names
If the first character of N (bytes or lines) is a '+', output begins with the Nth item from the start of each file, otherwise, print the last N items in the file. N bytes may be suffixed by k (x1024), b (x512), or m (1024^2).

head
head [OPTIONS] [FILE]...
Print first 10 lines of each FILE to standard output. With more than one FILE, precede each with a header giving the file name. With no FILE, or when FILE is -, read standard input.
Options:
        -n NUM Print first NUM lines instead of first 10
        -c NUM Output the first NUM bytes
        -q Never output headers giving file names
        -v Always output headers giving file names
cut
cut [OPTIONS] [FILE]...
Print selected fields from each input FILE to standard output
Options:
        -b LIST Output only bytes from LIST
        -c LIST Output only characters from LIST
        -d CHAR Use CHAR instead of tab as the field delimiter
        -s Output only the lines containing delimiter
        -f N Print only these fields
        -n Ignored

grep
grep [-HhrilLnqvsoweFEABCz] PATTERN [FILE]...
Search for PATTERN in each FILE or standard input
Options:
        -H Prefix output lines with filename where match was found
        -h Suppress the prefixing filename on output
        -r Recurse
        -i Ignore case distinctions
        -l List names of files that match
        -L List names of files that do not match
        -n Print line number with output lines
        -q Quiet. Return 0 if PATTERN is found, 1 otherwise
        -v Select non-matching lines
        -s Suppress file open/read error messages
        -c Only print count of matching lines
        -o Show only the part of a line that matches PATTERN
        -m MAX Match up to MAX times per file
        -w Match whole words only
        -F PATTERN is a set of newline-separated strings
        -E PATTERN is an extended regular expression
        -e PTRN Pattern to match
        -f FILE Read pattern from file
        -A Print NUM lines of trailing context
        -B Print NUM lines of leading context
        -C Print NUM lines of output context
        -z Input is NUL terminated

ps
ps
Report process status
Options:
        -o col1,col2=header Select columns for display
        -T Show threads
kill
kill [-l] [-SIG] PID...
Send a signal (default: TERM) to given PIDs (-9 forces shutdown)
Options:
        -l List all signal names and numbers
ifconfig
ifconfig [-a] interface [address]
Configure a network interface
Options:
        [-]broadcast [ADDRESS]] [[-]pointopoint [ADDRESS]]
        [netmask ADDRESS] [dstaddr ADDRESS]
        [outfill NN] [keepalive NN]
        [hw ether|infiniband ADDRESS] [metric NN] [mtu NN]
        [[-]trailers] [[-]arp] [[-]allmulti]
        [multicast] [[-]promisc] [txqueuelen NN] [[-]dynamic]
        [mem_start NN] [io_addr NN] [irq NN]
        [up|down] ...
iptables
Usage: iptables -[AD] chain rule-specification [options]
       iptables -[RI] chain rulenum rule-specification [options]
       iptables -D chain rulenum [options]
       iptables -[LFZ] [chain] [options]
       iptables -[NX] chain
       iptables -E old-chain-name new-chain-name
       iptables -P chain target [options]
       iptables -h (print this help information)

Commands:
Either long or short options are allowed.
  --append -A chain Append to chain
  --delete -D chain Delete matching rule from chain
  --delete -D chain rulenum
        Delete rule rulenum (1 = first) from chain
  --insert -I chain [rulenum]
        Insert in chain as rulenum (default 1=first)
  --replace -R chain rulenum
        Replace rule rulenum (1 = first) in chain
  --list -L [chain] List the rules in a chain or all chains
  --flush -F [chain] Delete all rules in chain or all chains
  --zero -Z [chain] Zero counters in chain or all chains
  --new -N chain Create a new user-defined chain
  --delete-chain
        -X [chain] Delete a user-defined chain
  --policy -P chain target
        Change policy on chain to target
  --rename-chain
        -E old-chain new-chain
        Change chain name, (moving any references)
Options:
  --proto -p [!] proto protocol: by number or name, eg. `tcp'
  --source -s [!] address[/mask]
        source specification
  --destination -d [!] address[/mask]
        destination specification
  --in-interface -i [!] input name[+]
        network interface name ([+] for wildcard)
  --jump -j target
        target for rule (may load target extension)
  --goto -g chain
        jump to chain with no return
  --match -m match
        extended match (may load extension)
  --numeric -n numeric output of addresses and ports
  --out-interface -o [!] output name[+]
        network interface name ([+] for wildcard)
  --table -t table table to manipulate (default: `filter')
  --verbose -v verbose mode
  --line-numbers print line numbers when listing
  --exact -x expand numbers (display exact values)
[!] --fragment -f match second or further fragments only
  --modprobe=<command> try to insert modules using this command
  --set-counters PKTS BYTES set the counter during insert/append
[!] --version -V print package version.

vi
vi [OPTIONS] [FILE]...
Edit FILE
Options:
        -R Read-only - do not write to the file
# Commonly used commands
## ifconfig – configure a network interface
ifconfig is used to display or modify (static) network interface settings. It can be used to change the interface state to on (up) or off (down), change the IP-address or networkmask of an interface or add virtual interfaces (multiple IP-addresses on one NIC).
NOTE: ifconfig cannot be used to configure a NIC with DHCP. ifconfig will however overwrite any IP-address settings done using DHCP.
Without parameters ifconfig will list the current IP configuration:
# ifconfig
eth0 Link encap:Ethernet HWaddr 00:90:E8:15:8A:9E
        inet addr:172.16.1.101 Bcast:172.16.255.255 Mask:255.255.0.0
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        RX packets:486 errors:0 dropped:0 overruns:0 frame:0
        TX packets:1477 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000
        RX bytes:115641 (112.9 KiB) TX bytes:167366 (163.4 KiB)
        Interrupt:25
The following command sets the IP-address and networkmask of interface “eth1”:
# ifconfig eth1 192.168.1.1 netmask 255.255.0.0
# ifconfig
eth0 Link encap:Ethernet HWaddr 00:90:E8:15:8A:9E
        inet addr:172.16.1.101 Bcast:172.16.255.255 Mask:255.255.0.0
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        RX packets:486 errors:0 dropped:0 overruns:0 frame:0
        TX packets:1477 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000
        RX bytes:115641 (112.9 KiB) TX bytes:167366 (163.4 KiB)
        Interrupt:25

eth1 Link encap:Ethernet HWaddr 00:90:E8:15:8A:9F
        inet addr:192.168.1.1 Bcast:192.168.255.255 Mask:255.255.0.0
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        RX packets:0 errors:0 dropped:0 overruns:0 frame:0
        TX packets:1412 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000
        RX bytes:0 (0.0 B) TX bytes:163038 (159.2 KiB)
        Interrupt:27
The following command adds a virtual interface with it's own IP-address:
# ifconfig eth1:0 192.168.1.2 netmask 255.255.0.0
# ifconfig
eth0 Link encap:Ethernet HWaddr 00:90:E8:15:8A:9E
        inet addr:172.16.1.101 Bcast:172.16.255.255 Mask:255.255.0.0
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        RX packets:486 errors:0 dropped:0 overruns:0 frame:0
        TX packets:1477 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000
        RX bytes:115641 (112.9 KiB) TX bytes:167366 (163.4 KiB)
        Interrupt:25

eth1 Link encap:Ethernet HWaddr 00:90:E8:15:8A:9F
        inet addr:192.168.1.1 Bcast:192.168.255.255 Mask:255.255.0.0
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        RX packets:0 errors:0 dropped:0 overruns:0 frame:0
        TX packets:1412 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000
        RX bytes:0 (0.0 B) TX bytes:163038 (159.2 KiB)
        Interrupt:27

eth1:0 Link encap:Ethernet HWaddr 00:90:E8:15:8A:9F
        inet addr:192.168.1.2 Bcast:192.168.255.255 Mask:255.255.0.0
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        Interrupt:27
The example below turns the interface “eth1” off:
# ifconfig eth1 down
# ifconfig
eth0 Link encap:Ethernet HWaddr 00:90:E8:15:8A:9E
        inet addr:172.16.1.101 Bcast:172.16.255.255 Mask:255.255.0.0
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        RX packets:486 errors:0 dropped:0 overruns:0 frame:0
        TX packets:1477 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000
        RX bytes:115641 (112.9 KiB) TX bytes:167366 (163.4 KiB)
        Interrupt:25
NOTE: when an interface is turned off, all virtual interfaces associated with it will be turned off as well.
## dhcpcd
dhcpcd is used to configure a network interface using DHCP.
# dhcpcd eth1
The command above acquires an IP address for eth1 using DHCP.
NOTE: dhcpcd will exit after applying the acquired network settings.
## route
## dnsmasq
## iptables – firewall, port-forwarding and NAT-router
iptables the control interface for the “netfilter” modules which can be loaded into the kernel. These modules provide extensive options to filter and redirect network traffic. Together with iptables it's possible to create a firewall, do port-forwarding and configure advanced NAT rules.
NOTE: loading more modules into the linux kernel increases it's memory and CPU usage. In embedded environments like the Moxa it's recommended only to load required modules. So if no firewall or NAT functionality is required, don't load the netfilter kernel modules.
iptables is based on the concept of tables and chains. A chain is a list of rules which are evaluated until a match is found after which the system moves on to the next chain. A table is a collection of chains for a specific mode of operation (NAT or filter). The chains are executed (their rules evaluated) in a specific order. The way the system executes the different chains is illustrated in illustration 1. If a kernel module isn't loaded (like mangle or nat) the chains contained within these tables are skipped.

Illustration 1: Execution of netfilter tables and chains
NOTE: ip forwarding (or routing) is disabled by default. To enable ip-forwarding the following command should be executed:
# echo 1 > /proc/sys/net/ipv4/ip_forward

Table	Chain	Function
Filter	FORWARD	Filters packets to servers accessible by another NIC on the firewall.
	INPUT	Filters packets destined to the firewall.
	OUTPUT	Filters packets originating from the firewall
Nat	PREROUTING	Address translation occurs before routing. Facilitates the transformation of the destination IP address to be compatible with the firewall's routing table. Used with NAT of the destination IP address, also known as destination NAT or DNAT
	POSTROUTING	Address translation occurs after routing. This implies that there was no need to modify the destination IP address of the packet as in pre-routing. Used with NAT of the source IP address using either one-to-one or many-to-one NAT. This is known as source NAT, or SNAT

Table 1: netfilter chains

A chain contains rules and a default target. Every rule consists of match criteria and a target. Once the criteria of a single rule are matched, the system “jumps” to the target for further processing. If all the rules are evaluated without mathing any criteria, the system jumps to the default target. Table 2 shows the most common options to specify match criteria.

iptables command Switch	Description
-t <-table->	If you don't specify a table, then the filter table is assumed. As discussed before, the possible built-in tables include: filter, nat, mangle
-j <target>	Jump to the specified target chain when the packet matches the current rule.
-A	Append rule to end of a chain
-F	Flush. Deletes all the rules in the selected table
-p <protocol-type>	Match protocol. Types include, icmp, tcp, udp, and all
-s <ip-address>	Match source IP address
-d <ip-address>	Match destination IP address
-i <interface-name>	Match "input" interface on which the packet enters.
-o <interface-name>	Match "output" interface on which the packet exits
--dport <portnr>	Match destination port

Table 2: Most commonly used match criteria options

target	Desciption	Common Options
ACCEPT	iptables stops further processing. / The packet is handed over to the end application or the operating system for processing	N/A
DROP	iptables stops further processing. / The packet is blocked	N/A
REJECT	Works like the DROP target, but will also return an error message to the host sending the packet that the packet was blocked	--reject-with qualifier / The qualifier tells what type of reject message is returned.
NAT	Used to do destination network address translation i.e. rewriting the destination IP address of the packet	--to-destination ipaddress / Tells iptables what the destination IP address should be
SNAT	Used to do source network address translation i.e. rewriting the source IP address of the packet / The source IP address is user defined	--to-source <address>[-<address>][:<port>-<port>] / Specifies the source IP address and ports to be used by SNAT.
MASQUERADE	Used to do Source Network Address Translation. / By default the source IP address is the same as that used by the firewall's interface	[--to-ports <port>[-<port>]] / Specifies the range of source ports to which the original source port can be mapped.

Table 3: iptable targets
### Examples: Saving and loading firewall rules
# iptables-save > /etc/firewall
Save the current firewall rules to the file /etc/firewall. The file /etc/firewall will be overwritten.
# iptables-restore --no-flush < /etc/ipod-interface
Append the contents of the file /etc/ipod-interface to any existing firewall rules.
NOTE: The iptables-restore command replaces all firewall rules by default. Use the option --no-flush to append.
### Examples: Port-forwarding and MANY:1 NAT
For this example a Moxa has two configured interfaces: an internal interface (eth0) with ip-address 192.168.1.40, and an external interface (eth1) with ip-address 10.0.0.40. The Moxa will be configured as internet gateway (MANY:1 NAT) and port-forwarding will be configured on the external interface to be able to use the iPhone app.

# iptables -t nat -A PREROUTING -i eth1 -p tcp -d 10.0.0.40 --dport 28401 -j DNAT --to 192.168.1.50
# iptables -P INPUT DROP
# iptables -A INPUT -i eth1 -m state --state ESTABLISHED,RELATED -j ACCEPT
# iptables -A FORWARD -i eth0 -o eth1 -j ACCEPT
# iptables -A FORWARD -i eth1 -o eth0 -m state --state ESTABLISHED,RELATED -j ACCEPT
# iptables -t nat -A POSTROUTING -o eth1 -j MASQUERADE
#### Step by step:
# iptables -t nat -A PREROUTING -i eth1 -p tcp -d 10.0.0.40 --dport 28401 -j DNAT --to 192.168.1.50
Add a rule to the chain PREROUTING of the nat table which will apply to packets arriving on interface eth1 using tcp protocol and port 28401 and apply DNAT to 192.168.1.50.
# iptables -P INPUT DROP
Set the default target for chain INPUT of the filter table (implicitly specified by omitting the -t option) in op DROP.
# iptables -A INPUT -i eth1 -m state --state ESTABLISHED,RELATED -j ACCEPT
Add a rule to chain INPUT of the filter tablle which applies to packets that arrived on eth1 and which has a TCP-port that has the status ESTABLISHED or RELATED and ACCEPT them. This rule enables packets which are sent to the Moxa using a connection that has already been established to pass through to the Moxa itself.
# iptables -A FORWARD -i eth0 -o eth1 -j ACCEPT
Add a rule to the chain FORWARD of the filter table which applies to packets that arrived on eth0 and will be sent on eth1. This rule will allow ip-forwarding for packets originating from the internal network with an IP-address on the external network as destination. This rule is required to be able to use the Moxa as an internet gateway.
NOTE: This rule doesn't allow any response from the external network to go back through to the internal network!
# iptables -A FORWARD -i eth1 -o eth0 -m state --state ESTABLISHED,RELATED -j ACCEPT
Add a rule to the chain FORWARD of the filter table which aplies to packets that arrived on eth1 and will be sent on eth0 and have a TCP-port that has the status ESTABLISHED or RELATED and ACCEPT them.
# iptables -t nat -A POSTROUTING -o eth1 -j MASQUERADE
Add a rule to the chain POSTROUTING of the nat table which applies to packets that will be sent on eth1 and apply MASQUERADE. This will rewrite the “source” address in the packets to the ip-address of the Moxa. Every connection is tracked so that the original source address is retained. When packets return to the moxa they are routed back to the original soruce address. This is often referred to as MANY:1 NAT.
### Examples: 1:1NAT internal to external TCP
For this example a Moxa has two internal IP addresses (eth0) 192.168.1.1 and 192.168.1.2 and two external IP addresses(eth1) 10.0.0.1 en 10.0.0.2. There are nodes on the internal network that need to be able to communicate with a node on the external network with IP address 10.0.0.3 using TCP port 502 (Modbus/TCP).
# iptables -t nat -A PREROUTING -p tcp -d 192.168.1.2 -–dport 502 -j DNAT --to 10.0.0.3
# iptables -A FORWARD -p tcp –-dport 502 -d 10.0.0.3 -j ACCEPT
# iptables -t nat -A POSTROUTING -d 10.0.0.3 -j SNAT --to 10.0.0.2
# iptables -A FORWARD -i eth1 -o eth0 -m state --state ESTABLISHED,RELATED -j ACCEPT
#### Step by step:
# iptables -t nat -A PREROUTING -p tcp -d 192.168.1.2 -–dport 502 -j DNAT --to 10.0.0.3
Add a rule to the chain PREROUTING of the nat table that applies to packets with destination 192.168.1.2 and destination port 502 and redirects them using DNAT to 10.0.0.3.
# iptables -A FORWARD -p tcp –-dport 502 -d 10.0.0.3 -j ACCEPT
Add a rule to the chain FORWARD of the filter table which applies to packets with destination 10.0.0.3 and destination port 502 and ACCEPTs them.
# iptables -t nat -A POSTROUTING -d 10.0.0.3 -j SNAT --to 10.0.0.2
Add a rule to the chain POSTROUTING of the nat table which applies to packets with destination 10.0.0.3 and change the source to 10.0.0.2 using SNAT.
# iptables -A FORWARD -i eth1 -o eth0 -m state --state ESTABLISHED,RELATED -j ACCEPT
Add a rule to the chain FORWARD of the filter table which applies to packets that arrived on eth0 and will be sent on eth0 of which the TCP port has status ESTABLISHED or RELATED and ACCEPT them.
### Examples: 1:1 NAT
For this example the Moxa has been configured with two internal (eth0) IP addresses: 192.168.1.1 and 192.168.1.2 and two external (eth1) IP addresses: 10.0.0.1 and 10.0.0.2. There is a device on the internal network (192.168.1.3) that needs to be able to communicate with a device on the external network (10.0.0.3) and vice-versa.
# iptables -t nat -A PREROUTING -d 192.168.1.2 -j DNAT --to 10.0.0.3
# iptables -A FORWARD -s 192.168.1.3 -d 10.0.0.3 -j ACCEPT
# iptables -t nat -A POSTROUTING -s 10.0.0.3 -j SNAT --to 192.168.1.2
# iptables -t nat -A PREROUTING -d 10.0.0.2 -j DNAT --to 192.168.1.3
# iptables -A FORWARD -s 10.0.0.3 -d 192.168.1.3 -j ACCEPT
# iptables -t nat -A POSTROUTING -s 192.168.1.3 -j SNAT --to 10.0.0.2
Step by step:
# iptables -t nat -A PREROUTING -d 192.168.1.2 -j DNAT --to 10.0.0.3
Add a rule to the chain PREROUTING of the nat table which redirect all packets with destination 192.168.1.2 to 10.0.0.3
# iptables -A FORWARD -s 192.168.1.3 -d 10.0.0.3 -j ACCEPT
Add a rule to the chain FORWARD of the filter table which will ACCEPT all packets with source address 192.168.1.3 and destination address 10.0.0.3.
# iptables -t nat -A POSTROUTING -s 10.0.0.3 -j SNAT --to 192.168.1.2
Add a rule to the chain POSTROUTING of the nat table which applies to packets with source address 10.0.0.3 and changes the source address to 192.168.1.2.
# iptables -t nat -A PREROUTING -d 10.0.0.2 -j DNAT --to 192.168.1.3
Add a rule to the chain PREROUTING of the nat table which applies to packets with destination address 10.0.0.2 and redirects them 192.168.1.3.
# iptables -A FORWARD -s 10.0.0.3 -d 192.168.1.3 -j ACCEPT
Add a rule to the chain FORWARD of the filter table which will ACCEPT packets with source address 10.0.0.3 and destination address 192.168.1.3.
# iptables -t nat -A POSTROUTING -s 192.168.1.3 -j SNAT --to 10.0.0.2
Add a rule to the chain POSTROUTING of the nat table which applies to packets with source address 192.168.1.3 changes the source address to 10.0.0.2.
## vi for dummies
vi is a text editor that has been around since 1976. It's a fairly primitive editor without graphical interface. Even so, 36% of Linux users still uses this editor (or it's slightly bigger brother vim).
vi is dramatically different to use than graphical text editors most people are used to. Without direction an unfamiliar user won't even be able to change a single character! However, with a few basic instructions it will become the fastest way to make small configuration changes on the Moxa.
### Modes
vi is a modal editor. The way vi reacts to input will change depending on the mode vi is in. The most important modes are command and insert mode. vi allways starts in command mode. Command mode enables the user to execute commands like copy, paste, cut, search and save. All commands are executed by pressing a key or key combination. Insert mode enables the user to insert text. Press <i> or <insert> in command mode to enter insert mode. Press <esc> in insert mode to return to command mode. Note that there is no indication of the current mode. Pressing the <esc> key twice will flash the screen and ensures vi is in command mode.
### Example: cutting/pasting a line and saving
# vi /etc/rc.custom
#!/bin/sh
# Config
MASK_ETH1=255.255.255.0
IP_ETH1=192.168.2.125
IP_ETH1_prefix=192.168.2.
IP_ETH0_prefix=192.168.1.
"/etc/rc.custom" line 1 of 75 --1%--
The green rectangle is the cursor. Pressing <dd> (<d> twice) cuts the current line:
# Config
MASK_ETH1=255.255.255.0
IP_ETH1=192.168.2.125
IP_ETH1_prefix=192.168.2.
IP_ETH0_prefix=192.168.1.
"/etc/rc.custom" [modified] line 1 of 74 --1%--
Pressing <p> pastes the cut line after the current line:
# Config
#!/bin/sh
MASK_ETH1=255.255.255.0
IP_ETH1=192.168.2.125
IP_ETH1_prefix=192.168.2.
IP_ETH0_prefix=192.168.1.
"/etc/rc.custom" [modified] line 2 of 74 --2%--
Pressing <:w> and <enter> writes (saves) the file:
# Config
#!/bin/sh
MASK_ETH1=255.255.255.0
IP_ETH1=192.168.2.125
IP_ETH1_prefix=192.168.2.
IP_ETH0_prefix=192.168.1.
:w<enter>

# Config
#!/bin/sh
MASK_ETH1=255.255.255.0
IP_ETH1=192.168.2.125
IP_ETH1_prefix=192.168.2.
IP_ETH0_prefix=192.168.1.
"/etc/rc.custom" line 2 of 75 --2%--
### Example: inserting text
Press <i> to go to insert mode. In insert mode vi responds much in the same way as most modern text editors do. The <del> key doesn't work as expected though. The result. Below is the result of pressing <i> and typing “test<del>”:
tesT#!/bin/sh
# Config
MASK_ETH1=255.255.255.0
IP_ETH1=192.168.2.125
IP_ETH1_prefix=192.168.2.
IP_ETH0_prefix=192.168.1.
"/etc/rc.custom" [modified] line 1 of 75 --1%--
As shown above, pressing <del> capitalizes the text under the cursor. To remove the character under the cursor in insert mode press <backspace>. In command mode pressing <x> will do what <del> does in a regular text editor. To undo this little 'mistake' return to command mode by pressing <esc> and press <U> (shift+u). This will undo all changes in the current line. It's possible to undo one (1) action.
## Scripting
A shell script is a text file that contains shell commands. When the executable bit of the file is set, the commands in this file can be executed automatically by running the file. The commands that can be used in a script are the same commands used on the commandline. This makes shell-scripts an easy way to automate things. An example of a shell-script is /etc/rc.custum which is executed at startup.
### Shell
A shell is a command processing application. It presents the user with a prompt, and executes any commands the user types into the prompt. The first line of a shell script defines the shell it is run in. The line starts with #! directly followed by the full path of the shell to execute. There are numerous different shells. The most popular ones are: sh(shell), bash(born again shell), ash (NetBSD sh) and zsh. Different shells behave in slightly different ways. The most commonly used shell is sh. This document will describe the behavior of sh.
### Debugging
Shell scripts are generally executed very fast, and it can be hard to check weather everything completed successfully. To get more detail about the execution of commands, values of variables, and order of execution the script can be called with the -x flag. Below is an example of calling a script with the -x flag.
#cat testscript
#!/bin/sh
variable="Hello World"
echo $variable
#./testscript
Hello World
#sh -x testscript
+ variable='Hello World'
+ echo Hello World
Hello World
#
### Variables
If a value is assigned to a variable name, the value can be reused by placing a $ before the variable name. If a command is assign to a variable, this variable can be executed. If the variable is a number, it can be incremented.
#cat testscript
#!/bin/sh
command="echo"
variable=1
$command $variable
variable=$(($variable+1))
$command $variable

#sh -x testscript
+ command=echo
+ variable=1
+ echo 1
1
+ variable=2
+ echo 2
2
#

### if then else
It's possible to test for certain conditions and execute certain commands if these conditions are met. Conditions are written as an expression which returns true or 0. Commands can be part of the expression as well.
Comparisons:
-eq	equal to
-ne	not equal to
-lt	less than
-le	less than or equal to
-gt	greater than
-ge	greater than or equal to

File Operations:
-s	file exists and is not empty
-f	file exists and is not a directory
-d	directory exists
-x	file is executable
-w	file is writable
-r	file is readable

#cat testscript
#!/bin/sh
command="echo"
variable=1
if [ $variable -ge 5 ]
  then
    $command $variable
  else
    ping -c 1 google.com > /dev/null
    if [ $? -eq 0 ]
      then
      variable=$(($variable+1))
      $command $variable
      fi
fi

#sh -x testscript
+ command=echo
+ variable=1
+ '[' 1 -ge 5 ']'
+ ping -c 1 google.com
+ '[' 0 -eq 0 ']'
+ variable=2
+ echo 2
2
### Loops
It's possible to execute commands in a loop. There are two kinds of loops: for loops and while loops. A for loop is used to iterate a list, and a while loop is used to run until an expression evaluates to true. The example below show how to ping a range of IP-Adresses using both while and for loops.
#cat testscript
#!/bin/sh
variable=1
while [ $variable -le 10 ]
  do
    ping -c 1 -w 1 10.58.235.$variable > /dev/null
    if [ $? -eq 0 ]
      then
      echo FOUND ONE! @ 10.58.235.$variable
    fi
    variable=$(($variable+1))
  done
for host in {1..10}
  do
    ping -c 1 -w 1 10.58.235.$host > /dev/null
    if [ $? -eq 0 ]
      then
      echo FOUND ONE! @ 10.58.235.$host
    fi
done

#sh -x testscript
+ variable=1
+ '[' 1 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.1
+ '[' 0 -eq 0 ']'
+ echo FOUND 'ONE!' @ 10.58.235.1
FOUND ONE! @ 10.58.235.1
+ variable=2
+ '[' 2 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.2
+ '[' 1 -eq 0 ']'
+ variable=3
+ '[' 3 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.3
+ '[' 1 -eq 0 ']'
+ variable=4
+ '[' 4 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.4
+ '[' 1 -eq 0 ']'
+ variable=5
+ '[' 5 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.5
+ '[' 1 -eq 0 ']'
+ variable=6
+ '[' 6 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.6
+ '[' 0 -eq 0 ']'
+ echo FOUND 'ONE!' @ 10.58.235.6
FOUND ONE! @ 10.58.235.6
+ variable=7
+ '[' 7 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.7
+ '[' 1 -eq 0 ']'
+ variable=8
+ '[' 8 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.8
+ '[' 1 -eq 0 ']'
+ variable=9
+ '[' 9 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.9
+ '[' 1 -eq 0 ']'
+ variable=10
+ '[' 10 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.10
+ '[' 1 -eq 0 ']'
+ variable=11
+ '[' 11 -le 10 ']'
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.1
+ '[' 0 -eq 0 ']'
+ echo FOUND 'ONE!' @ 10.58.235.1
FOUND ONE! @ 10.58.235.1
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.2
+ '[' 1 -eq 0 ']'
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.3
+ '[' 1 -eq 0 ']'
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.4
+ '[' 1 -eq 0 ']'
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.5
+ '[' 1 -eq 0 ']'
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.6
+ '[' 0 -eq 0 ']'
+ echo FOUND 'ONE!' @ 10.58.235.6
FOUND ONE! @ 10.58.235.6
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.7
+ '[' 1 -eq 0 ']'
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.8
+ '[' 1 -eq 0 ']'
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.9
+ '[' 1 -eq 0 ']'
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.10
+ '[' 1 -eq 0 ']'

A second way to do simple if/then operations is using && or ||. When concatenating two commands together with && the first command (or expression) is executed, and the second is only executed if the first evaluates to 0. When using || the second command is only executed if the first command fails (doesn't return 0). The previous example can be simplified significantly using these concatenations.
#cat testscript
#!/bin/sh
variable=1
while [ $variable -le 10 ]
  do
    ping -c 1 -w 1 10.58.235.$variable > /dev/null && echo FOUND ONE! @ 10.58.235.$variable
    variable=$(($variable+1))
  done
for host in {1..10}
  do
    ping -c 1 -w 1 10.58.235.$host > /dev/null && echo FOUND ONE! @ 10.58.235.$host
done
#sh -x testscript
+ variable=1
+ '[' 1 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.1
+ echo FOUND 'ONE!' @ 10.58.235.1
FOUND ONE! @ 10.58.235.1
+ variable=2
+ '[' 2 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.2
+ variable=3
+ '[' 3 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.3
+ variable=4
+ '[' 4 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.4
+ variable=5
+ '[' 5 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.5
+ variable=6
+ '[' 6 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.6
+ echo FOUND 'ONE!' @ 10.58.235.6
FOUND ONE! @ 10.58.235.6
+ variable=7
+ '[' 7 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.7
+ variable=8
+ '[' 8 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.8
+ variable=9
+ '[' 9 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.9
+ variable=10
+ '[' 10 -le 10 ']'
+ ping -c 1 -w 1 10.58.235.10
+ variable=11
+ '[' 11 -le 10 ']'
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.1
+ echo FOUND 'ONE!' @ 10.58.235.1
FOUND ONE! @ 10.58.235.1
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.2
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.3
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.4
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.5
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.6
+ echo FOUND 'ONE!' @ 10.58.235.6
FOUND ONE! @ 10.58.235.6
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.7
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.8
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.9
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.10
## Parallel execution
The example above can take a long time to complete, especially if there are only two hosts in the network. Imagine scanning hundreds of hosts, of which only a few are powered on. To speed up the process it's possible to run several commands in parallel. To run a command as a seperate process, place a & sign after the command. This will return the process ID and resume script execution immediately. Please note that it isn't possible to use the return value of a command that is executed this way! The example below shows how to ping a range of network hosts in parallel, and a comparison in execution time of the sequential and parallel ping scripts.
#cat testscript
#!/bin/sh
for host in {1..10}
  do
    ( ping -c 1 -w 1 10.58.235.$host > /dev/null && echo FOUND ONE! @ 10.58.235.$host )&
done
wait
#sh -x testscript
+ for host in '{1..10}'
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.1
+ for host in '{1..10}'
+ for host in '{1..10}'
+ for host in '{1..10}'
+ for host in '{1..10}'
+ for host in '{1..10}'
+ for host in '{1..10}'
+ echo FOUND 'ONE!' @ 10.58.235.1
FOUND ONE! @ 10.58.235.1
+ for host in '{1..10}'
+ for host in '{1..10}'
+ ping -c 1 -w 1 10.58.235.2
+ wait
+ ping -c 1 -w 1 10.58.235.9
+ ping -c 1 -w 1 10.58.235.5
+ ping -c 1 -w 1 10.58.235.7
+ ping -c 1 -w 1 10.58.235.3
+ ping -c 1 -w 1 10.58.235.4
+ ping -c 1 -w 1 10.58.235.10
+ ping -c 1 -w 1 10.58.235.6
+ ping -c 1 -w 1 10.58.235.8
+ echo FOUND 'ONE!' @ 10.58.235.6
FOUND ONE! @ 10.58.235.6
As can be seen from the output, the script completes before the second host has been pinged. Moreover the hosts aren't pinged in the order the ping processes has been started! This is important to keep in mind when using parallel execution.
#time sh sequential
FOUND ONE! @ 10.58.235.1
FOUND ONE! @ 10.58.235.6

real 0m8.050s
#time sh parallel
FOUND ONE! @ 10.58.235.6
FOUND ONE! @ 10.58.235.1

real 0m1.031s
Executing commands in parallel clearly has it's advantages. In this case it speeds up execution by factor 8. Different commands will generate different results, and executing commands in parallel uses more system resources (memory/CPU).
## Troubleshooting
# Useful links and sources
http://www.busybox.net/downloads/BusyBox.html (NOTE! Documentation is for a different version, might differ from what is available on the Moxa)
http://en.wikibooks.org/wiki/Learning_the_vi_Editor
http://www.linuxhomenetworking.com/wiki/index.php/Quick_HOWTO_:_Ch14_:_Linux_Firewalls_Using_iptables

# Vi Cheat Sheet
## Modes

Vi has two modes insertion mode and command mode. The editor begins in command mode, where the cursor movement and text deletion and pasting occur. Insertion mode begins upon entering an insertion or change command. [ESC] returns the editor to command mode (where you can quit, for example by typing :q!). Most commands execute as soon as you type them except for "colon" commands which execute when you press the ruturn key.

Quitting
:x	Exit, saving changes
:q	Exit as long as there have been no changes
ZZ	Exit and save changes if any have been made
:q!	Exit and ignore any changes

## Inserting Text
i	Insert before cursor
I	Insert before line
a	Append after cursor
A	Append after line
o	Open a new line after current line
O	Open a new line before current line
r	Replace one character
R	Replace many characters

Motion
h	Move left
j	Move down
k	Move up
l	Move right
w	Move to next word
W	Move to next blank delimited word
b	Move to the beginning of the word
B	Move to the beginning of blank delimted word
e	Move to the end of the word
E	Move to the end of Blank delimited word
(	Move a sentence back
)	Move a sentence forward
{	Move a paragraph back
}	Move a paragraph forward
0	Move to the begining of the line
$	Move to the end of the line
1G	Move to the first line of the file
G	Move to the last line of the file
nG	Move to nth line of the file
:n	Move to nth line of the file

## Deleting Text
Almost all deletion commands are performed by typing d followed by a motion. For example, dw deletes a word. A few other deletes are:

x	Delete character to the right of cursor
X	Delete character to the left of cursor
D	Delete to the end of the line
dd	Delete current line
:d	Delete current line

## Yanking Text
Like deletion, almost all yank commands are performed by typing y followed by a motion. For example, y$ yanks to the end of the line. Two other yank commands are:

yy	Yank the current line
:y	Yank the current line

## Changing text
The change command is a deletion command that leaves the editor in insert mode. It is performed by typing c followed by a motion. For wxample cw changes a word. A few other change commands are:

C	Change to the end of the line
cc	Change the whole line

## Putting text
p	Put after the position or after the line
P	Put before the poition or before the line

Search for strings
/string	Search forward for string
?string	Search back for string
n	Search for next instance of string
N	Search for previous instance of string

# Moxa default settings
	Default IP Address	Netmask
LAN 1	192.168.3.127	255.255.255.0
LAN 2	192.168.4.127	255.255.255.0

Table 2: Default network settings
Baudrate	19200 bps
Parity	None
Data bits	8
Stop bit(s)	1
Flow Control	None
Terminal	VT100

Table 3: Serial connection settings
Login	root
Password	root

Table 4: Default login credentials